## Slide 1: The European power system
Ove Wolfgang, SINTEF Energy
ZEN PhD course, 2nd February 2018
- from an economist's perspective

## Slide 2: Content of presentation
Electricity as a product
Power markets – an introduction
Europe – decarbonization and internal market

## Slide 3: 1. Electricity as a product

## Slide 4: Electricity as a product
Modern societies are totally dependent on electricty (lighting, electrical appliances, etc).
It cost far less than the utility it provides
Producers and consumers are connected through an electrical grid
Electric energy travels almost with the speed of light, which takes 0,13 sec around the world.
There must be a a balance between feed-in and outtake from the grid at all times
There are CO2 emissions from fossil-fuel power generation, not from electricity consumption.
MWh: Energy
MW: Power
1 MW in 1 hour = 1 MWh

## Slide 5: How much would you be willing to pay each year for mobile charging?
Yearly electricity cost ~ 3 Euro per year (7 kWh)
The difference adds to social welfare

## Slide 6: 2. Power markets – an introduction

## Slide 7: Deregulation of power markets
Deregulation started as late as the 1990s
  First in in Norway, GB, New Zealand
  Power companies were split into producers and grid companies
  Organized market clearing in a power exchange
Before deregulation (Norway)
  Power companies were responsible for electricity supply in their area (generation, grid, …)
  Power prices were set annualy by the parliament, based on long-term costs

## Slide 8: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange

## Slide 9: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Choose a power supplier
Pay for electric energy and grid tariff (and taxes etc)

## Slide 10: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Produce electricity
Sell it e.g. at the exchange
E.g. Statkraft

## Slide 11: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Buy electricity at exchange
Sell retail, housholds etc
E.g.Norgesenergi

## Slide 12: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Builds enough grid (if not: KILE)
Charge a tariff for the utilization of their grid
Local (natural) monopolies, with regulated income cap
E.g. NTE

## Slide 13: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Responsible for transmission grid
Security of supply for national power system
Operates markets for ancillary services
Statnett
Calculate losses, market capacities, …

## Slide 14: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Overall responsibility for the whole power system (efficiency, security)
Concessions
NVE
Regulator: Systems, rules, regulation
TSO: Practical implementation for transmission grid

## Slide 15: Roles in power market
Consumers
Producers
Power suppliers
Grid company/DSO
Transmission system operator
Regulator
Power exchange
Organized / optimized market-clearing
Day-ahead, intraday
Nord Pool

## Slide 16: New roles are emerging (but not so much in Norway yet)
Prosumers
  Consumer
  And producer (e.g. PV)
  Feed-in support + cost reductions PV and batteries
Aggregators
  To aggregate consumer flexibiliby
  Offer a flexibility service to DSO/TSO?

## Slide 17: Market clearing at power exchanges (simplified representation)
Price (Euro/MWh)
Quantity (MWh)
Demand curve (marginal utility)
Wind
Hydro
Nuclear
Gas
Supply curve (marginal costs)

## Slide 18: Market equilibrium
Price (Euro/MWh)
Quantity (MWh)
Demand curve
Supply curve
Q
P

## Slide 19: Economic surplus
Price (Euro/MWh)
Quantity (MWh)
Demand curve
Supply curve
Q
P
VLL
Consumer suprlus
Producer suprlus

## Slide 20: Well-functioning markets are efficient
Price (Euro/MWh)
Quantity (MWh)
Demand curve
Supply curve
Q
VLL
Total surplus
Area is maximized

## Slide 21: Sources to inefficiencies in markets
Externalities
  E.g. pollution
  Solution: Put a tax on the externality
Market power
Missing markets
Public goods
Bounded rationality

## Slide 22: Congestion management
Problem: Calculated power flow from market clearing could be higher than capacity of transmission grid
Solution methods:
  TSO redispatch (e.g. within Germany)
  Price areas (within Nordic region)
  TSO special regulation (within price areas)

## Slide 23: Electricity markets and products
Day-ahead
Intraday
Ancillary services (operated by TSOs)
  Activated energy ("balancing markets")
  Reserve capacity
  FCR, FRR, RR; up and down
Financial markets
Note: Physical markets are (mostly) set up to handle forecast errors and deviations from day-ahead to the actual opeation!
Operated by power exchanges (e.g. Nord Pool)

## Slide 24: Norwegian hydropower
About 98 % of electricity generation in Norway
Highly flexible
Reservoir capacity
  About 85 TWh, i.e. 2/3 of annual consumption
  More than needed for balancing of RES in Europe (limitation is MW capacity)
Year-to-year variation in inflows to reservoirs
Stochastic optimizaiton is balance between i.a.:
  Head of water in reservoirs (efficiency)
  Save water to high-price periods (e.g. winter)
  Avoid spillage from reservoirs (before winter)

## Slide 25: Reservoir levels, whole Norway
Source: NVE

## Slide 26: 3. Europe: Decarbonization and internal market

## Slide 27: Power generation in EU 28
Source:
"Dash for gas"
"Energiewende"

## Slide 28: Policy instruments and tecnology costs
Policy
  Support for renewables
  Emission permit market
  EU ETS (make drawing)
Reduced costs for PV and batteries

## Slide 29
MAJOR cost reductions for PV and batteries
Kilde: IEA World Energy Investment 2016

## Slide 30
Stortingsmelding 25 (2015-2016)

## Slide 31
Emission cuts by sector (from EU Energy Roadmap 2050)

## Slide 32: We have only seen the start for RES!

## Slide 33: How to balance RES variability?
Controllable capacity (e.g. gas-power)
Energy storages (reservoirs, batteries, P2G, PS, …)
Demand response
Grid
Common market
Curtailment (load, RES)

## Slide 34: Intraday will become more important!
Previously, many countries had feed-in tariffs (fixed price) and priority dispatch (not to be regulated down) for RES
Response to too "easy" curtailment of RES if needed, unfair
New regulation: balancing responsibility also for RES
Balancing responsibility RES + more RES capacity = increase the importance of intraday markets

## Slide 35: EUs internal market for electricity
2008 Florence Forum European regulators: Target Model for integration of European electricity markets
3rd Energy package (2007); ACER, ENTSO-E
Network codes & guidelines (EEA relevance)
Market regulation adopted
  CACM (day-ahead, intraday, transmission capacity calc, clearing)
  EB (ancillary services, and TSO cooperation)
Day-ahead
Intraday
Balancing
Forwards
Transmission capacity calculation

## Slide 36: Implementation
Active contributions from industry stakeholders, including TSOs, regulators and power exchanges
Day-ahead markets in 19 European countries connected, 85% of consumption, EUPHEMIA algorithm
Intraday markets, XBID go live 13th March?
Balancing markets
  A more step-by-step careful approach for TSO cooperation
  But long term goals (Commission) are fully integrated markets

## Slide 37: Laconic from ENTSO-E
  "
  As the Balancing Services are the last resort action for TSOs to ensure Operational Security, the most important objective in developing integrated Balancing Markets is to keep the lights on while facilitating market integration.
  "
ENTSO-E (2013), "SUPPORTING DOCUMENT FOR THE NETWORK CODE ON ELECTRICITY BALANCING", p. 9.

## Slide 38: Graabak I and Korpås M (2016), "Variability Charactheristics of European Wind and Solar Power Resources – A Review", Energies. Bye T and Hope E (2005), "Deregulation of electricity markets – The Norwegian experience", Discussion Papers No. 433, September 2005, Statistics Norway, Research Department. Stortingsmelding 25 (2015-2016), "Kraft til endring – Energipolitikken mot 2030", Olje- og energidepartementet. (in Norwegian) OJ L 197/24 (2015), "Establishing a guideline on capacity allocation and congestion management", text with EEA relevance. EU commission (2011), "Impact Assessment accompanying the document Energy Roadmap 2050", Commission staff working paper, SEC(2011), 1565/2. Part 1/2.
Suggested reading